## Slide 1: Good practice for providing INSPIRE Coverage data and services
INSPIRE Community Forum
Elevation, Orthoimagery, Reference systems and Geographical grids
Observations & Measurements
Software & Tools
Jordi Escriu & Peter Baumann & Kathi Schleidt

## Slide 2: INSPIRE Coverages Summary
Coverage – What is it?
Identification of issues (October 2014 - today)
  Inconsistencies: INSPIRE conceptual model vs. Implementation standard (CIS 1.0).
    Lack of clarity of the standards for implementing coverages existing at that point of time (GML 3.2.1, GML 3.3, CIS 1.0).
    Possible misinterpretation (not ample experience on them).
    Immaturity and inconsistencies of the standards in place.
  INSPIRE added additional properties and model constructs not expected in an OGC-compliant implementation (i.e. not appropriately mapped).
Scope
  INSPIRE Thematic Clusters (October 2014 - May 2019).
  INSPIRE Community Forum (From June 2019).
Team involved
  Jordi Escriu (IDEC – ICGC, Catalunya).
  Peter Baumann (Jacobs University + rasdaman, Germany).
  Kathi Schleidt (DataCove.eu, Austria).

## Slide 3: Implementation of INSPIRE Coverages Main activities run till today
“Implementation of INSPIRE Coverages” – Webinar
6th November 2017
  https://inspire.ec.europa.eu/forum/pages/view/159283/webinar-implementation-of-inspire-coverages
“Practicing INSPIRE coverages - Enhancing your data cube implementation assets!” – Workshop
INSPIRE Conference 2018 Antwerp:
  https://inspire.ec.europa.eu/events/conferences/inspire_2018/submissions/248.doc
“Feel the power of INSPIRE WCS/WCPS in your hands!” – Workshop
INSPIRE Helsinki 2019:
  https://inspire.ec.europa.eu/forum/pages/view/262985/workshop-%E2%80%9Cfeel-the-power-of-inspire-wcs-wcps-in-your-hands%E2%80%9D
  “INSPIRE Coverages demystified” (Description) - Dedicated session:
  Online INSPIRE Conference 2020 (10th June 2020) – Presentations + Video:
  https://inspire.ec.europa.eu/conference2020/webinars/inspire-coverages-demystified

## Slide 4: INSPIRE Coverages Modelled at conceptual level
D2.10.2 v1.0
INSPIRE Data specifications –
Base Models –
Coverage types
OGC 09-146r1
GML Coverage application schema
<<featureType>>
<Theme-specific coverage class 1>
<<featureType>>
<Theme-specific coverage class N>
…
INSPIRE Data models
(Conceptual level)
Implementation standards
(Implementation level)
OGC 09-146r2
CIS 1.0
GML Application Schema for Coverages
?
INSPIRE Themes

## Slide 5: INSPIRE Coverages Common seed model for all INSPIRE themes
D2.10.2 v1.0
INSPIRE Data specifications –
Base Models –
Coverage types
abstract
<<featureType>>
CoverageByDomainAndRange
domainSet (any type)
rangeSet (any type)
rangeType (RecordType type)
metadata (any type)
Domain constrained to CV_Grid (*)
<<featureType>>
RectifiedGridCoverage
Domain constrained to
CV_RectifiedGrid (*)
Regular domain
Regular grids
<<featureType>>
ReferenceableGridCoverage
Domain constrained to CV_ReferenceableGrid (*)
Irregular domain
Irregular grids

## Slide 6: Use of coverages in INSPIRE 13 Data themes
INSPIRE
Coverages
EL
LC
GE
OI
SO
LU
NZ
EF
AC
MF
OF
ER
SD
WCS view: Coverages as Features
SOS view: Coverages as Observation Results

## Slide 7: WCS view: Coverages as Features INSPIRE FeatureTypes based on Coverage Classes
Regular grids:
  Elevation (EL)
  Land cover (LC)
  Orthoimagery (OI)
  Soil (SO)
  Energy resources (ER).
  Species distribution (SD) - Application schema deprecated.
Regular or Irregular grids:
  Natural risk zones (NZ)
  Geology (GE).
INSPIRE
Coverages
EL
LC
GE
OI
SO
LU
NZ
EF
AC
MF
OF
ER
SD

## Slide 8: SOS view: Coverages as Observation Results Coverage based models in the observational context
INSPIRE
Coverages
EL
LC
GE
OI
SO
LU
NZ
EF
AC
MF
OF
ER
SD
Regular or irregular grids
  Environmental monitoring facilities (EF)
  Atmospheric conditions (AC)
  Meteorological geographic features (MF)
  Oceanographic geographic features (OF)
  Geology (GE)
Provided as discrete observation coverages, i.e. gridded data specialized observation types applying the ISO 19156:2011 (O&M), following INSPIRE D2.9 v3.0

## Slide 9: SOS view: Coverages as Observation Results Coverage based models in the observational context
D2.9 v3.0
INSPIRE Guidelines for the use of
Observations & Measurements and Sensor Web Enablement-related standards
in INSPIRE Annex II and III data specification development
Based on ISO 19156:2011 Observations and Measurements standard (O&M in OGC)
Use of Gridded Data specialized observation types.
EF
AC
MF
OF

## Slide 10: Implementation of INSPIRE Coverage What is exactly the issue? INSPIRE Extensions
INSPIRE
Conceptual
model
2
7
3
4
1
9
0
2
8
metadata
range type
INSPIRE
Extensions
INSPIRE
Implementation model
(PROPOSAL)
2
7
3
4
1
9
0
2
8
INSPIRE Cov
Metadata
range type
OGC CIS1.0
Implementation model
2
7
3
4
1
9
0
2
8
metadata
range type

## Slide 11: Good Practice for providing INSPIRE Coverage data and services An interoperable solution
The proposed solution
  Getting feedback from the community on this functional good practice to align INSPIRE coverages to OGC standards.
  Promote our interoperable schemas for their widespread use by the thematic communities dealing with coverage data for INSPIRE purposes:
    Directly adopt OGC CIS 1.0 schema as default implementation model.
    Replace the existing INSPIRE coverage schemas by our INSPIRE coverage metadata schemas (i.e. consider INSPIRE extensions as coverage metadata).
  Please do USE these schemas!!

## Slide 12: Good Practice for providing INSPIRE Coverage data and services Documentation + Discussion
Documentation & Discussion
  Discussion document:
  https://inspire.ec.europa.eu/forum/file/view/266799/discussion-document-good-practice-for-providing-raster-inspire-coverage-data-and-services
  Dedicated page:
  https://inspire.ec.europa.eu/forum/pages/view/265454/an-effective-good-practice-to-boost-interoperable-provision-of-raster-inspire-coverage-data-and-services
  Discussion topic (for providing feedback):
  https://inspire.ec.europa.eu/forum/discussion/view/265095/inspire-coverages-demo-service

## Slide 13: INSPIRE Coverages Demystified Website and Demonstrator
https://inspire.rasdaman.org/

## Slide 14: Implementation of INSPIRE Coverages More details about this work
“INSPIRE coverages: an analysis and some suggestions” - Article with first suggestions:
  https://link.springer.com/article/10.1186%2Fs40965-019-0059-x
Documentation of past activities (See Slide 3)
Results & Demos from the “INSPIRE Coverages demystified” session (Online INSPIRE Conference 2020), focused on OI, EL, LC:
https://inspire.ec.europa.eu/conference2020/webinars/inspire-coverages-demystified
  INSPIRE coverage (metadata) schemas.
  Examples of WCS/WCPS services.
  Examples of INSPIRE coverage metadata.

## Slide 15: Good Practice for providing INSPIRE Coverage data and services Discussion
Objectives
  Getting feedback from the community on this functional good practice to align INSPIRE coverages to OGC standards.
  Spread the word through INSPIRE MIG-T for its consideration and promotion.
  Promote the use of the amended, interoperable schemas proposed in this good practice.
  Engage specific data providers in adopting this good practice.
Potential next steps
  Looking forward to got it endorsed.
  Get a critical mass of use.
  Document it using the INSPIRE good practice template.
  Revise the necessary items of INSPIRE framework (schemas, TGs, etc.).
Discussion

## Slide 16: Thanks for your attention!
Jordi Escriu
jordi.escriu@icgc.cat
Peter Baumann
baumann@rasdaman.com
Kathi Schleidt
kathi@DataCove.eu